## Slide 1: Time Synchronization over Bluetooth Low Energy
Milin Patel

## Slide 2: Approach
Use timeslot API for accurate send and receive
16 MHz timer as sync timer
PPI used to avoid CPU involvement and allow hardware to trigger on events
One node in system chosen as timing master
Used reference code found online so mostly focused on integrating the reference code and analyzing/testing it

## Slide 3: Sending a Sync Packet
The timeslot API provides access to radio hardware for a configurable period of time.
A timer is used that matches the ramp up time of the radio to ensure that we read the sync timer as close to the packet transmission as possible.

## Slide 4: Receiving a Packet
When a packet arrives, a radio interrupt is triggered that the CPU can service and then read the sync information.
A “magical” value is used to account for the time spent sending the packet, receiving it in the radio hardware, triggering an interrupt, and the CPU servicing the interrupt.
The timer value in the sync packet is compared to the local timer and an offset is found that is applied to the local timer.

## Slide 5: Test Setup
Integrated reference code into a basic blinky example from Nordic.
Implemented a basic BLE service and single characteristic that allows another device like a smartphone to choose who the timing master is (0x0 for slave, 0x1 for master).
Setup 2 GPIOs, one to toggle on every timer counter increment, one to go high when a node becomes the master.
Hooked up a logic analyzer to monitor those GPIO on all nodes.

## Slide 6: Analysis – Before Sync
We can see that before sync, the nodes clearly are not synchronized. The difference in the edges is anywhere between 500us-1.5ms.

## Slide 7: Analysis – Immediately After Sync
We can see immediately after the first sync packet is sent out; the edges are within 80-200ns of each other.

## Slide 8: Analysis – Drift until next sync packet
In this image, we can see the difference in the edges a couple milliseconds before the next sync packet arrives. They are around ~500ns apart as 1 node is more unsynchronized than the others.

## Slide 9: Conclusion
Great way to get sub microsecond time synchronization over BLE.
Limited to Nordic devices as it requires SoftDevice.
Would be useful to see it added to the BLE standard in future versions.